## Slide 1: Dealing with physical units in modern C++

## Slide 2: About me
Nikola Jelić, embedded engineer, ~11years of experience
Working in Zuehlke Engineering for the last 4.5 years
Studied computer science at Faculty of Mathematics, Belgrade, Serbia
Great fan of:
  Linux; mature, diverse, solid OS for embedded and many other use cases
  C; effectively the macro assembly, but portable 
  modern C++; 11 and beyond, when functional and generic programming began to take shape
  Haskell; the most complete functional language out there (to my knowledge)

## Slide 3: Background
Real world measurements require strict physical units
Embedded devices, by their nature, interact with physical world – either through sensors or through actuators
It is common to work with: length, speed, acceleration, volume, mass, pressure, electric current, electric potential, electric resistance, time, temperature, etc.
Challenges of dealing with real world measurements:
  Precision of measurements
  Speed of acquiring measurements (usually in direct opposition with precision)
  Precision of calculations
  Consistency of units – the subject of the presentation

## Slide 4: The problem
It was common to mark variables and arguments (usually with suffixes) in order to designate the exact physical unit it represents (e.g. mass_kg, volume_ml)
Unfortunately, this is prone to human errors, and not consistent across code bases
Additional problem with the units: mass can be expressed in kg, g, but also in tons, pounds, ounces, etc.
Adding conversion functions for all possible combinations is difficult and error prone
It would be great if we could put all the consistency checks into compiler – the bad code would simply not compile

## Slide 5: International System of Units - SI
The big seven: A, K, s, m, kg, cd and mol
Short history – there were dozens of unit systems in the world, and it took decades to consolidate them into the metric system
There are still places in the world that use the Imperial system (USA, Liberia and Myanmar)
Huge benefits for science and commerce
All other standard units can be expressed through these seven; example V = kg·m2·s−3·A−1
All non-SI units can also be expressed as derivatives, usually with some additional calculations; example [°F] = [K] × ​9⁄5 − 459.67

## Slide 6: Real project requirements
Device has to deal with heating and dispensing water (e.g. tea preparation)
No third party library may be added, only self-made solutions are acceptable
Typical units in the system (non-exhaustive list):
  Time in hours, seconds and milliseconds (~70% of all units used, OS + business logic)
  Volume in litres, millilitres and microlitres (~12% of all units used, business logic)
  Temperature in Celsius and Kelvin (~12% of all units used, business logic)
  Frequency in Hz; electric current in milliamperes and microamperes; electric potential in volts, millivolts and microvolts; electric resistance in milliohms; flow in millilitres per second, etc.
Zero (or very small) runtime overhead, both in instructions and memory
Code refactoring should eliminate all unit inconsistencies, and make the code more readable

## Slide 7: Modern C++ approach
C++11, C++14 and beyond
The biggest benefit of modern C++ is not its object-orientation, but generic and functional paradigms
Template programming + constexpr methods allows us to have all of the type checks and majority of conversions done in the compile time
Suffix operators improve readability (e.g: 10_ms, 14_l, etc.)
Std::ratio allows us to store conversion factors within the type itself, and makes conversion between the units of same dimensionalities trivial (e.g. interval_ms = unit_cast<milliseconds>(16_s))
Distinction between an absolute value and interval, similar to the one seen in chrono library

## Slide 8
Step by step

## Slide 9: The basic physical unit
template <typename ValType, typename Factor, typename LenDim, typename MassDim,
typename TimeDim, typename ElcurDim, typename TempDim, typename AmmDim,
typename LumDim>
class PhysicalUnit {...}
ValType may be an int, float, double or any number type
Factor should always be a std::ratio, in order to allow units of the same dimensionalities, but different scale (e.g. litres, millilitres, etc.). All units have this factor in the relation to the base unit (e.g. one litre is 1/1000 of m3)
Seven dimensions could be integers, but std::ratios are better solution, in order to support fractional dimensions (square roots and similar edge cases)

## Slide 10: Conversion constructor
class PhysicalUnit { …
explicit PhysicalUnit(const PhysicalUnit<V, F, LenDim, MassDim, TimeDim, ElcurDim, TempDim, AmmDim, LumDim> &val) {
using outRatio = std::ratio_divide<F,Factor>;
m_value = val.value() * outRatio::num / outRatio::den;
} … }
Compiler will generate only the conversions that we are going to use in the code, so the overhead is minimal
The explicit keyword is intentional – we don’t want “accidental” conversions

## Slide 11: Comparisons
Could have been easier with C++20 <=> spaceship operator
template <typename V1, typename V2, typename ...Ts>
inline constexpr bool operator==(const PhysicalUnit<V1, Ts...> &lhs,
const PhysicalUnit<V2, Ts...> &rhs) {
return lhs.value() == rhs.value();
}
We should only compare the physical units which has same dimensionality and factor
Variadic templates give us conciseness, because all of the template arguments must match – seven dimensions AND conversion factor

## Slide 12: Addition and subtraction
The easy ones
template < typename V1, typename V2, typename ...Ts>
auto
operator+(const PhysicalUnit<V1, Ts...> &lhs,
const PhysicalUnit<V2, Ts...> &rhs) ->
PhysicalUnit<decltype(lhs.value() + rhs.value()), Ts...> {
return PhysicalUnit<decltype(lhs.value() + rhs.value()), Ts...>(lhs.value() + rhs.value());
}
Similar to the comparisons, we only add and subtract values of the same type, but we can infer the return type

## Slide 13: Multiplication and division I
Working with scalars, simple case
template <typename V1, typename V2, typename ...Ts>
constexpr auto
operator*(const V1 &lhs, const PhysicalUnit<V2, Ts...> &rhs) ->
PhysicalUnit<decltype(lhs * rhs.value()), Ts...> {
return PhysicalUnit<decltype(lhs * rhs.value()), Ts...>(lhs * rhs.value());
}
Not a big deal for multiplications, division is only trivial if we divide physical unit with a scalar
The type is again inferred

## Slide 14: Multiplication and division II
Working with scalars, not so simple case
template <typename V1, typename V2, typename F, typename LD, typename MD, typename TD, typename ED, typename TMD, typename AD, typename LUD, >
constexpr auto
operator/(const V1 &lhs, const PhysicalUnit<V2, F, LD, MD, TD, ED, TMD, AD, LUD> &rhs)
-> PhysicalUnit<decltype(lhs / rhs.value()), std::ratio_divide<std::ratio<1>,F>, std::ratio_subtract<std::ratio<0>,LD>,…> {
return PhysicalUnit<decltype(lhs / rhs.value()), std::ratio_divide<std::ratio<1>,F>, std::ratio_subtract<std::ratio<0>,LD>,…> (lhs / rhs.value());
}
The return type is derived by inversing the conversion factor and negating the dimensions

## Slide 15: Multiplication and division III
Working with other physical units
template <typename V1, typename F1, typename LD1,…, typename V2, typename F2, typename LD2,…>
constexpr auto operator*(const PhysicalUnit<V1, F1, LD1, …> &lhs,
const PhysicalUnit<V2, F2, LD2, …> &rhs) ->
PhysicalUnit<decltype(lhs.value() * rhs.value()), std::ratio_multiply<F1,F2>, std::ratio_add<LD1,LD2>,…> {
return PhysicalUnit<decltype(lhs.value() * rhs.value()), std::ratio_multiply<F1,F2>, std::ratio_add<LD1,LD2>,…>(lhs.value() * rhs.value());
}
Similar to the scalar case, but now both values have their factors and dimensions

## Slide 16: Converting to scalars
No accidental castings allowed
template <typename ValType, typename Factor>
class PhysicalUnit <ValType, Factor, std::ratio<0>, …>{
constexpr operator ValType() const {
return m_value * Factor::num / Factor::den;
}
}
Template specialization is very handy here
We allow casting to the underlying type if all dimensions are zero (dimensionless value)

## Slide 17: Absolute physical units
Similar, but not the same
Rationale: we measure time from some time point, not the absolute amount of time from the beginning of the universe
Time point and time interval are already separated nicely by std::chrono
Similar situations arises with temperature – we deal with temperature differences in some calculations, and with absolute temperature in others.
A lot of attributes are shared (factor, dimensions), but the behaviour is different:
  Subtracting two time points yields a time interval
  Adding or subtracting time interval from a time point yields a time point
  Comparisons work the same way as with standard physical units
  No multiplications or divisions are allowed

## Slide 18: Basic absolute physical unit
template <typename ValType, typename DiffType, typename Factor, typename LenDim, typename MassDim, typename TimeDim, typename ElcurDim, typename TempDim, typename AmmDim, typename LumDim>
class AbsolutePhysicalUnit {
public:
using DiffPhysicalUnit = PhysicalUnit<DiffType, Factor, LenDim, MassDim, TimeDim, ElcurDim, TempDim, AmmDim, LumDim>;
…}
We establish a relation between an absolute unit (e.g. time) and a physical unit used for representing the difference between two absolute unit points (e.g. time difference between two dates represented in seconds, hours or days)

## Slide 19: Subtracting two absolute units
class AbsolutePhysicalUnit {
constexpr DiffPhysicalUnit operator-(const AbsolutePhysicalUnit& rhs) const
{
return DiffPhysicalUnit(value() - rhs.value());
} … }
Very simple implementation, because templates do all the work for us

## Slide 20: Adding an absolute unit and a normal one
template <typename ValType, typename ...Ts>
constexpr AbsolutePhysicalUnit<ValType, Ts...> operator+(const PhysicalUnit<Ts...>& lhs,
const AbsolutePhysicalUnit<ValType, Ts...>& rhs) {
return AbsolutePhysicalUnit<ValType, Ts...>(lhs.value() + rhs.value());
}
Again, very simple, due to the templates

## Slide 21: Creating specific units
// Volume
/// @brief Unit for litres, 10^-3 m^3
using Litre_t = PhysicalUnit<float, std::milli, std::ratio<3>, std::ratio<0>, std::ratio<0>, std::ratio<0>, std::ratio<0>, std::ratio<0>, std::ratio<0>>;
constexpr Litre_t operator"" _l(uint64_t val) { return Litre_t(static_cast<float>(val)); };
constexpr Litre_t operator"" _l(long double val) { return Litre_t(static_cast<float>(val)); };
Litre is expressed as number of metres cubed, which is correct
We can now use constants in the code such as 10_l, 3.5_l, etc. which is really cool
All derived units are expressed strictly as a combination of the base units, with the corresponding conversion factor.
This implementation doesn’t cover k*x + n conversions, needed for Celsius to Fahrenheit

## Slide 22
Summary

## Slide 23: Lessons learned
Templates are getting more and more powerful in modern C++
Suffixes improve code readability significantly
We should push more and more checks into the compile time
Sometimes not being able to use an already existing solution can be a great call for adventure and learning 
Creation of types could possibly be made prettier
Cloud parts of IoT projects could benefit from this approach, since they face same challenges when dealing with telemetry data on the server side
The eight dimension is sometimes added – the angle; useful for rotations per second and other calculation pertaining to circular motion

## Slide 24
Thank you 